## Slide 1: Management Information Systems: Managing the Digital Firm
Seventeenth Edition, Global Edition
Chapter 7
Telecommunications, the Internet, and Wireless Technology
Copyright © 2022, 2020, 2018 Pearson Education, Ltd. All Rights Reserved
Slide in this Presentation Contain Hyperlinks. JAWS users should be able to get a list of links by using INSERT+F7
Notes: If this PowerPoint presentation contains mathematical equations, you may need to check that your computer has the following installed:
1) MathType Plugin
2) Math Player (free versions available)
3) NVDA Reader (free versions available)

## Slide 2: Learning Objectives
7.1 What are the principal components of telecommunications networks and key networking technologies?
7.2 What are the different types of networks?
7.3 How do the Internet and Internet technology work, and how do they support communication and e-business?
7.4 What are the principal technologies and standards for wireless networking, communication, and Internet access?
7.5 How will M I S help my career?
Notes: This chapter discusses the principal technologies used in networking and the Internet. Ask students what the difference is between a network and the Internet. Why is networking so important to modern organizations? How many students have wireless networks at home? How many have a smartphone that uses a 4G or 5G network? What's the difference between a 4G network and Wi-Fi? How many students have seen an RFID tag?

## Slide 3: Video Cases
Case 1: Telepresence Moves out of the Boardroom and into the Field
Case 2: Virtual Collaboration with I B M Sametime

## Slide 4: Alibaba: Redefining Traditional Retailing (1 of 2)
Problem
  omnichannel retail strategy
  supply chain
Solutions
  Hema app
  curating through QR codes

## Slide 5: Alibaba: Redefining Traditional Retailing (2 of 2)
The Hema app continuously acquires information from its customers
Demonstrates I T’s role in helping organizations increase efficiency and lower costs
Illustrates the ability of I T systems to support inventory management and sales

## Slide 6: Networking and Communication Trends
Convergence
  Telephone networks and computer networks converging into single digital network using Internet standards
Broadband
  Majority of U.S. households have high-speed broadband
Broadband wireless
  Voice, data communication are increasingly taking place over broadband wireless platforms
Notes: This slide discusses recent developments in networking technologies. Ask students to give an example of convergence. How fast is broadband today? Note that in 2000, typical Internet access speeds were 56 kbps over a telephone line, costing 25 cents per kilobit, whereas today broadband speeds are 5-500 mbps, costing a fraction of a cent per kilobit. Are students aware of how fast their Internet connections are at home, school, or work? Ask students if they know the speed of their cell phone’s Internet connection. The point here is to try and raise awareness of telecommunications systems among students.

## Slide 7: What Is a Computer Network?
Two or more connected computers
Major components in simple network
  Client and server computers
  Network interfaces (N I C s)
  Connection medium
  Network operating system (N O S)
  Hubs, switches, routers
Software-defined networking (S D N)
  Functions of switches and routers managed by central program
Notes: This slide describes what a network is along with the components that you will find in a simple network (illustrated on the next slide.) Ask students to describe the function of an NIC. What is a connection medium? Ask students to describe the purpose of a hub, switch, and router.

## Slide 8: Figure 7.1 Components of a Simple Computer Network
Notes: Figure 7.1, Page 252.
Illustrated here is a simple computer network consisting of computers, a network operating system (NOS) residing on a dedicated server computer, cable (wiring) connecting the devices, switches, and a router.
Although the NOS is shown as part of the server, note that, depending on the type of software, an NOS may also be designed to reside on client computers (these are called peer-to-peer networks). Do some students have a home computer network? Ask them to describe the elements of the network.
Alt Text
Long description: A flow diagram explains the various components of a simple computer network. The sequence is as follows:
PC computer
Switch. This is connected to another PC.
Switch. This is connected to a a network operating system server.
Router
Other networks/internet.

## Slide 9: Networks in Large Companies
Large number of local area networks (L A N s) linked to firmwide corporate networks
Various powerful servers
  Website, corporate intranet, extranet
  Backend systems
Mobile wireless L A N s (Wi-Fi networks)
Videoconferencing system
Telephone network, wireless cell phones
Notes: This slide looks at the additional components one might expect to find in the network of a large company that has many locations and thousands of employees (illustrated on the next slide). Ask students what is meant by “backend systems.” Note that many firms are dispensing with traditional landline telephone networks and using Internet telephones that run on existing internal data networks and the Internet.

## Slide 10: Figure 7.2 Corporate Network Infrastructure
Notes: Figure 7.2, Page 253.
Today’s corporate network infrastructure is a collection of many networks from the public switched telephone network, to the Internet, to corporate local area networks linking workgroups, departments, or office floors.
This graphic illustrates the components of a large company’s network. Note the difference between the wireless LAN, which allows wireless access within the office, and the mobile Wi-Fi network, which allows Internet access to employees outside of offices. The advantage of telephone-based wireless systems is that they do not require a Wi-Fi hotspot to work, and in fact can connect users to the entire globe through their telephone networks. Cable networks—major competitors of telephone company Internet providers—have recently developed a mobile option. Optimum Cable (Comcast) has installed neighborhood Wi-Fi hot spots, allowing cable subscribers wireless access to the Internet.
Alt Text
Long description: Two flow diagrams explain the infrastructure of a corporate network. The first flow diagram illustrates a connection between the mobile phone, smartphones and the telephone system, which is connected to the telephone service provider.
At the center of the second flow diagram is the internet service provider which is connected to the following:
A series of servers depicting the corporate website intranet and extranet.
Internet. The internet is connected to the mobile Wi-Fi network via the wireless internet service provider.
Wireless LAN through the corporate wired network.

## Slide 11: Key Digital Networking Technologies (1 of 3)
Client/server computing
  Distributed computing model
  Clients linked through network controlled by network server computer
  Server sets rules of communication for network and provides every client with an address so others can find it on the network
  Has largely replaced centralized mainframe computing
  The Internet: largest implementation of client/server computing
Notes: This slide and the following two look at the main technologies in use today for networks: client/server computing, packet switching, and TCP/IP. Ask students what advantages client/server computing has over centralized mainframe computing.

## Slide 12: Key Digital Networking Technologies (2 of 3)
Packet switching
  Method of slicing digital messages into parcels (packets), sending packets along different communication paths as they become available, and then reassembling packets at destination
  Previous circuit-switched networks required assembly of complete point-to-point circuit
  Packet switching more efficient use of network’s communications capacity
Notes: This slide continues the discussion of the three main networking technologies today, looking at the second, packet switching. Note that circuit-switched networks were expensive and wasted available communications capacity—the circuit had to be maintained whether data was being sent or not. It is also important to note that packet switching enables packets to follow many different paths. What is the advantage of this capability? If one path is blocked due to an accident or power failure, the data will automatically be shifted by routers to open paths. However, in truly massive outages like the September 11, 2011 attack on the World Trade Center, nearby metropolitan servers were knocked out, and for a period of several days, Internet access was limited in the New York Metropolitan area. The notion that packet switching networks would survive a nuclear attack is highly unlikely.

## Slide 13: Figure 7.3 Packet-Switched Networks and Packet Communications
Notes: Figure 7.3, Page 255.
Data are grouped into small packets, which are transmitted independently over various communications channels and reassembled at their final destination.
This graphic illustrates how packet switching works, showing a message being split into three packets, sent along different routes, and then reassembled at the destination. Note that each packet contains a packet number, message number, and destination.

## Slide 14: Key Digital Networking Technologies (3 of 3)
T C P /I P and connectivity
  Protocols: rules that govern transmission of information between two points
  Transmission Control Protocol/Internet Protocol (T C P / I P)
    Common worldwide standard that is basis for the Internet
  Department of Defense reference model for T C P / I P
    Four layers
      Application layer
      Transport layer
      Internet layer
      Network interface layer
Notes: This slide continues the discussion of the three main networking technologies in use today and looks at the third, TCP/IP. Note that in a network, there are typically many different types of hardware and software components that need to work together to transmit and receive information. Different components in a network communicate with one another only by adhering to a common set of rules called protocols. In the past, many diverse proprietary and incompatible protocols often forced business firms to purchase computing and communications equipment from a single vendor. But today, corporate networks are increasingly using a single, common, worldwide standard called Transmission Control Protocol/ Internet Protocol (TCP/IP). TCP/IP actually is a suite of protocols, the main ones of which are TCP and IP. Ask students what these two main protocols are responsible for.

## Slide 15: Figure 7.4 The Transmission Control Protocol/Internet Protocol (T C P/I P) Reference Model
Notes: Figure 7.4, Page 256.
This figure illustrates the four layers of the TCP/IP reference model for communications.
Note that what happens when computer A sends a message to computer B, is that the data that computer A creates is transferred within that computer from the application layer to subsequent layers in sequence. In this process it is split into packets, and information is added at each stage, ultimately translating the packets into a form that can be transferred over the network interface. After traveling over the network interface, the packets are reassembled at the recipient computer, from the network interface layer up, ultimately for use by the application layer.
Alt Text
Long description: A figure illustrates how two computers using TCP/IP communicate. Computer A communicates to computer B through the four layers of the transmission control protocol/internet protocol reference model.
The four layers are:
Application
Transport
Internet
Network interface.

## Slide 16: Types of Networks
Signals: Digital versus analog
  Modem: translates digital signals into analog form (and vice versa)
Types of networks
  Local area networks (L A N s)
    Ethernet
    Client/server vs. peer-to-peer
  Wide area networks (W A N s)
  Metropolitan area networks (M A N s)
  Campus area networks (C A N s)
Notes: This slide looks at the types of networks that organizations use. Ask students what the differences are between digital and analog signals. Ask students to describe and distinguish between LANs, CANs, WANs, and MANs, and also to talk about their different range of operation. Note that a network can be defined by the way the clients interact (client/server versus peer-to-peer), the type of physical medium to carry signals (Ethernet, Fast Ethernet, etc.), and the way in which computers are connected and send signals to each other (topology).

## Slide 17: Figure 7.5 Functions of the Modem
Notes: Figure 7.5, Page 257.
A modem is a device that translates digital signals into analog form (and vice versa) so that computers can transmit data over analog networks such as telephone and cable networks.
This graphic illustrates the differences between digital and analog signals and shows how digital signals can be sent to other computers over analog cables such as telephone and cable lines which are analog. Note that digital signals are representations of the two binary digits, 0 and 1, and are represented logically as on and off electrical pulses (in reality as different voltages). Ask students what MODEM stands for.
Alt Text
Long description: An illustration explains how a computer translates digital signals into analog form. Computer sends digital signals in the form of bits and bytes to the modem. The modem then translates to the signal received into analog form for the following networks:
Telephone line
Cable system
Wireless media
Analog device.

## Slide 18: Transmission Media and Transmission Speed
Physical transmission media
  Twisted pair wire (C A T5 and CAT6)
  Coaxial cable
  Fiber optics cable
  Wireless transmission media and devices
    Satellites
    Cellular systems
Bandwidth: Transmission speed
  Bits per second (b p s)
  Hertz
  Bandwidth
Notes: This slide looks at the media involved in network transmission. Note that many of the telephone systems in buildings had twisted wires installed for analog communication, but they can be used for digital communication as well. Also, today, telecommunications companies are starting to bring fiber optic cable into the home for high-speed Internet access.
Note that the transmission capacity of a medium (bps) is dependent on its frequency, which is measured in hertz, or cycles per second. Ask students to define bandwidth (it is the difference between the highest and lowest frequencies that can be accommodated on a single channel).

## Slide 19: What Is the Internet?
The Internet
  World’s most extensive network
  Internet service providers (I S P s)
    Provide connections
    Types of Internet connections
      Dial-up: 56.6 K b p s
      Digital subscriber line (D S L/F I O S): 385 K b p s –100+ M b p s
      Cable Internet connections: 20–100 M b p s
      Satellite
      T1/T3 lines: 1.54 Mbps/45 M b p s
Notes: This slide examines what the Internet is—ask students to describe it and what they use it for. The text refers to the Internet as the most extensive public communication system and the world’s largest implementation of client/server computing.

## Slide 20: Internet Addressing and Architecture
Each device on Internet assigned Internet Protocol (I P) address
32-bit number, e.g. 207.46.250.119
The Domain Name System (D N S)
  Converts IP addresses to domain names
  Hierarchical structure
  Top-level domains
Notes: Ask students what an IP address is used for. Ask students why we have a domain name system, and why we don't just use IP addresses. Note that the domain name system makes it possible for people to remember addresses.
Ask students how they connect to the Internet. Do any use satellite? Note that T lines are leased, dedicated lines suitable for businesses or government agencies requiring high-speed guaranteed service levels. Do students know that the Internet does not guarantee any service level and agrees only to make a “best effort.”

## Slide 21: Figure 7.6 The Domain Name System
Notes: Figure 7.6, Page 260.
The Domain Name System is a hierarchical system with a root domain, top-level domains, second-level domains, and host computers at the third level.
This graphic describes how the domain name system works. Note that the “root” domain is the period that is used before the top-level domain, such as .edu or .com. Give students an example Internet address, such as myserver.myspace.com and ask them what the top-, second-, and third-level domains are.
Alt Text
Long description: A four-tier hierarchy explains the concept of the domain name system. The details of the hierarchy are as follows:
At the topmost level is the root domain.
The second level consists of top-level domains such as: edu, com, gov, org, net, and other domains.
The third level consists of second-level domains such as: expedia and google from the “com” domain and congress from the “gov” domain.
The fourth level consist of the third-level domains and host computers such as sales from the “google” domain.
The sales dot google dot com is connected to the host computer, labeled computer 1 and translates into computer1 dot sales dot google dot com.

## Slide 22: Internet Architecture and Governance
Network service providers
  Own trunk lines (high-speed backbone networks)
Regional telephone and cable T V companies
  Provide regional and local access
Professional organizations and government bodies establish Internet standards
  I A B
  I C A N N
  W 3 C
Notes: The Internet has many governmental, international, and professional bodies that govern its policies. In addition, many countries have created partially independent domestic Internets that are controlled by government intelligence agencies. The concept of a global Internet is no longer a reality. For instance, the Internet users experience in China or Iran is different from the Internet experienced in the United States, EU, and other Asian countries.

## Slide 23: Figure 7.7 Internet Network Architecture
Notes: Figure 7.7, Page 262.
The Internet backbone connects to regional networks, which in turn provide access to Internet service providers, large firms, and government institutions. Network access points (NAPs) and metropolitan area exchanges (MAEs) are hubs where the backbone intersects regional and local networks and where backbone owners connect with one another.
This graphic illustrates the architecture of the Internet. Note that MAEs (metropolitan area exchanges) are hubs where the backbone intersects regional and local networks and where backbone networks connect with one another.
Alt Text
Long description: An illustration explains Internet network architecture. The details of the network diagram are as below:
The internet backbone is interconnected to the MAE hub, which includes the regional hubs like the MAEs and NAPs.
The MAE is interconnected to the regional hosts and the MAE hub through the internet.
The regional host is connected to the domains like nyu dot edu and the local ISP through the T1 line.
POP3 mail and SMTP mail are transmitted from the domain: nyu dot edu.
The domain nyu dot edu is connected to the campus network and offices. The client IP address gets assigned here.
The domain local ISP through the regular phone line is connected to the home. The client IP address gets assigned here.

## Slide 24: The Future Internet: I P v 6 and Internet 2
I P v 6
  New addressing scheme for I P numbers
  Will provide more than a quadrillion new addresses
  Not compatible with earlier I P v 4 addressing
Internet2
  Advanced networking consortium
    Universities, businesses, government agencies, other institutions
  Developed high-capacity 100 G b p s testing network
  Testing leading-edge new technologies for Internet

## Slide 25: Internet Services and Communication Tools (1 of 2)
Internet services
  E-mail
  Chatting and instant messaging
  Newsgroups
  Telnet
  File Transfer Protocol (F T P)
  World Wide Web
Notes: This slide continues the discussion about what the Internet is, here looking at the services, or applications, that the Internet supports. Notice that the Internet comprises many more services than just e-mail and the web. Ask students which of these services, beyond e-mail and the web have they used, and if they have, to describe how it works.

## Slide 26: Internet Services and Communication Tools (2 of 2)
Voice over IP (VoIP)
  Digital voice communication using I P, packet switching
Unified communications
  Communications systems that integrate voice, data, e-mail, conferencing
Virtual private network (V P N)
  Secure, encrypted, private network run over Internet
Notes: Students who have cable Internet telephones are using VoIP. Other popular technologies that use the Internet as a platform are VoIP, unified communications, and virtual private networks. Ask students what they think is the value to business is of each of these technologies.

## Slide 27: Figure 7.8 Client/Server Computing on the Internet
Notes: Figure 7.8, Page 264.
Client computers running web browsers and other software can access an array of services on servers over the Internet. These services may all run on a single server or on multiple specialized servers.
This graphic looks at the services that an Internet server computer can offer: Websites (HTTP), e-mail (SMTP), file transfer (FTP), newsgroups (NNTP). It illustrates where on the path between client and backend systems these services lie.
Alt Text
Long description: A network diagram explains how client computers can access an array of services on servers over the Internet. The sequence of the flow is as follows:
The client computer or smartphone which is using web browser and other client software is interconnected to the internet. The internet is interconnected to the server. Both these interconnections are depicted via dashed bidirectional arrows.
The server includes the following:
Web (HTTP) server
Simple Mail Transfer Protocol (SMTP)
Domain Name Serving (DNS) utility
File Transfer Protocol (FTP)
Network News Transfer Protocol (NNTP)
The server is interconnected to the application server, web pages, and mail files.
The application server is further interconnected to the database server which is interconnected to the back-end systems. The back-end system includes various databases. The application server is also connected to the entities: Sales, production, accounting, and HR.

## Slide 28: Figure 7.9 How Voice over I P Works
Notes: Figure 7.9, Page 265.
A VoIP phone call digitizes and breaks up a voice message into data packets that may travel along different routes before being reassembled at the final destination. A processor nearest the call’s destination, called a gateway, arranges the packets in the proper order and directs them to the telephone number of the receiver or the IP address of the receiving computer.
This graphic shows how VoIP works. The voice messages are digitized and transported over the Internet in the same packet-switching method as traditional Internet data. Gateways are simply computers (network devices) that maintain the interface with the Internet in a firm.
Alt Text
Long description: A two-way flow diagram explains how voice over IP works. The details are as below:
Message from the user passes through the gateway via the internet and reaches the user at the other end and vice-versa.
The message “How are you?” which gets digitized as ABC and breaks up into data packets, while passing through the internet before being reassembled at the final destination.
The gateway near the user arranges the packets in the proper order and directs them to the receiving computer.
Similarly, the return message “Fine, thank you!” gets digitized as XYZ and breaks up into data packets before passing the gateway and resembling again for the user.

## Slide 29: Figure 7.10 A Virtual Private Network Using the Internet
Notes: Figure 7.10, Page 268.
This VPN is a private network of computers linked using a secure tunnel connection over the Internet. It protects data transmitted over the public Internet by encoding the data and wrapping them within the Internet protocol. By adding a wrapper around a network message to hide its content, organizations can create a private connection that travels through the public Internet.
This graphic illustrates how a virtual private network works. The rectangles A, B, C, and D represent different computers on the VPN. In a process called tunneling, packets of data are encrypted and wrapped inside IP packets. By adding this wrapper around a network message to hide its content, business firms create a private connection that travels through the public Internet.
Alt Text
Long description: An illustration explains the concept of virtual private network. The details are as follows:
The data tunnel which sends and receives data is at the center of the illustration.
The data tunnel is enclosed by the internet.
Bidirectional arrows connect computers A, B, C, and D to the data tunnel via the internet.

## Slide 30: Interactive Session: Management: Monitoring Employees on Networks: Unethical or Good Business?
Class discussion
  Should managers monitor employee e-mail and Internet usage? Why or why not?
  Describe an effective e-mail and web use policy for a company.
  Should managers inform employees that their web behaviour is being monitored? Or should managers monitor secretly? Why or why not?

## Slide 31: The Web
Hypertext
  Hypertext Markup Language (H T M L)
  Hypertext Transfer Protocol (H T T P):
  Uniform resource locator (U R L):
    http://www.megacorp.com/content/features/082602.html
Web servers
    Software for locating and managing web pages
Notes: This slide looks at one of the most popular services on the Internet, the web, and the main protocols enabling the web. The web is an interlinked connection of websites, which are collections of web pages linked to a home page. These pages are created using a text markup language call HTML and transmitted to user’s web browsers by HTTP. Web page addresses (URLs) are composed of the domain name of the website and the file location of the individual web page. Ask students if any have created web pages using HTML, and if so, to describe what this is like. How have they made the web pages visible to others on the web?

## Slide 32: Searching for Information on the Web
Search engines
Mobile search
Semantic search and predictive search
Visual search
Intelligent agent shopping bots
Search engine marketing
Search engine optimization (S E O)
Notes: This slide looks at how people find information of interest on the web. The primary method is through search engines, which today act as major portals to the web. Ask students where their initial points of entry are on the web, and how they find information they are interested in. Most will be Google users, but ask if they have looked at Bing, the Microsoft search engine that is showing some promise.
The text discusses how big the web is, in terms of pages. Google indexed an estimated 5 billion web pages in 2019, but this does not include the “deep web.” Other estimates point to “one trillion” web pages, but many of these are duplicates.

## Slide 33: Figure 7.11 Top Desktop/Laptop Web Search Engines Worldwide
Notes: Figure 7.11, Page 269.
Google is the most popular search engine.
Source: Based on data from Net Market Share, February 2020.
This graphic ranks the major search engines according to popularity, or percentage of total number of searches performed. Google is a clear favorite. Is this due to the superiority of their search engine results or does it involve other factors such as their clean interface, or their reach, which makes their ad platform more valuable to advertisers. Poll your class about the search engines they use.
Alt Text
Long description: A pie chart presents data on the market share of various search engines across the world. The details are as follows:
Google: 73.1%
Bing: 11.6%
Baidu: 10.4%
Yahoo: 2.5%
Others: 2.5%.

## Slide 34: Figure 7.12 How Google Works
Notes: Figure 7.12, Page 270.
The Google search engine is continuously crawling the web, indexing the content of each page, calculating its popularity, and storing the pages so that it can respond quickly to user requests to see a page. The entire process takes about half a second.
This graphic illustrates in a very high-level diagram how Google works. At the foundation of Google’s search engine are two concepts—page ranking and the indexing of combinations of words. Ask students if they have a favorite search engine, and if so, why that search is their favorite. The reality of how Google actually works is the subject of many volumes and is beyond the scope of this book.
Alt Text
Long description: A process diagram explains the various steps followed by Google web search. The details of the diagram are as follows:
Step 1: User enters query.
Step 2: Google’s Web servers receive the request. Google uses millions of servers linked together and connected to the internet to handle incoming requests and produce the results.
Step 3: Request is sent to Google’s index servers that describe which pages contain the keywords matching the query and where those pages are stored on the document servers.
Step 4: Using the PageRank software, the system measures the “importance” or popularity of each page by solving an equation with more than 500 million variables and two billion terms. These are likely the “best” pages for the query.
Step 5: Small text summaries are prepared for each Web page.
Step 6: Results delivered to user, 10 to a page.
All the steps in the diagram are shown as a sequence in the form of an enclosure, which begin and end at the user.

## Slide 35: Sharing Information on the Web
Blogs and microblogs
RSS
Wikis
Social networking
Notes: .

## Slide 36: The Future Web
More tools to make sense of trillions of pages on the Internet
Pervasive web
Internet of Things (I o T)
App Internet
Increased cloud computing and S a a S
Ubiquitous mobile connectivity
Greater seamlessness of web as a whole
Notes: The Internet of Things includes the idea that our cars, refrigerators, heaters and air conditioning units, along with all other appliances, and buildings, will be on the Internet.

## Slide 37: Interactive Session: Technology: Talking Cars Make for Better Road Safety
Class discussion
  What are the pros and cons of the V2X technology?
  What can be done to speed up the adoption of V2X technology among vehicle owners?
  What other applications can you think of for the ITS Connect?

## Slide 38: Cellular Systems (1 of 2)
Competing standards
  C D M A : United States only
    Verizon, Sprint
  G S M : Rest of world
    A T&T, T-Mobile
Third-generation (3G) networks
  144 K b p s
  Suitable for e-mail access, web browsing
Notes: This slide discusses the evolution in wireless communication. Ask students what changes or improvements have happened in their cell phone service over the past two years. Have they purchased or upgraded a cell phone in that time, and if so, why? 3G networks, a standard which first appeared in the early 2000s, have mobile upload capacities of about 144 mbps, enough for email and some web browsing, but not videos. 3G networks have been largely supplanted by more powerful 4G networks, with 5G an upcoming technology (discussed in the next slide).

## Slide 39: Cellular Systems (2 of 2)
Fourth-generation (4G) networks
  Up to 100 Mbps
  Suitable for Internet video
  L T E and WiMax
5G Networks
  Gigabit capacity
  Starting to be launched by AT&T, Verizon, and other carriers
Notes: This slide continues the discussion of the evolution in wireless communication. 4G networks started appearing in 2010 in the United States. They are also called LTE (Long Term Evolution) networks. 4G cell networks can be used for display of video on mobile devices with download speeds of about 100 mbps, and upload speeds of 50 mbps. 5G networks are just now beginning to be deployed and will enable movies to be downloaded in seconds. How many students watch videos on their smartphones?

## Slide 40: Wireless Computer Networks and Internet Access (1 of 2)
Bluetooth (802.15)
  Links up to 8 devices in 10-meter area using low-power, radio-based communication
  Useful for personal networking (P A N s)
Wi-Fi (802.11)
  Set of standards: 802.11
  Used for wireless L A N and wireless Internet access
  Use access points: device with radio receiver/transmitter for connecting wireless devices to a wired L A N
Notes: This slide discusses the current standards in wireless networking. Ask students if they have any Bluetooth or wireless devices they use for computing, such as keyboards, earphones, or other. Note that in most Wi-Fi communications, wireless devices communicate with a wired LAN using an access point.

## Slide 41: Wireless Computer Networks and Internet Access (2 of 2)
  Hotspots: one or more access points in public place to provide maximum wireless coverage for a specific area
  Weak security features
W i Max (802.16)
  Wireless access range of 31 miles
  Require W i M a x antennas
Notes: This slide continues the discussion about wireless networking and Wi-Fi. Ask students if they have ever connected to the Internet through a hotspot at an airport, coffee shop, hotel, or other location. Are they aware of the security issues of using their smartphones to access the Internet at, say, Starbucks.
Ask students what other drawbacks, beside security, there are to Wi-Fi (roaming difficulties, interference). Note that wireless networks based on the upcoming 802.11n specification will solve interference problems by using multiple wireless antennas in tandem to transmit and receive data and technology to coordinate multiple simultaneous radio signals. What is this technology called? (MIMO).

## Slide 42: Figure 7.13 A Bluetooth Network (P A N)
Notes: Figure 7.13, Page 278.
Bluetooth enables a variety of devices, including cell phones, smartphones, wireless keyboards and mice, PCs, and printers, to interact wirelessly with each other within a small, 30-foot (10-meter) area. In addition to the links shown, Bluetooth can be used to network similar devices to send data from one PC to another, for example.
This graphic illustrates the uses of Bluetooth for a PAN. Bluetooth connects wireless keyboards and mice to PCs or cell phones to earpieces without wires. Bluetooth has low-power requirements, making it appropriate for battery-powered handheld computers, and cell phones. Most cell phones today are Bluetooth enabled, allowing them to connect to other wireless devices (such as earphones) and PCs.
Alt Text
Long description: An illustration explains a sample Bluetooth network. In the diagram, the printer communicates with various devices through a private connection. The various devices shown in the diagram are:
Smartphones
Wireless Keyboard
User Computer

## Slide 43: Figure 7.14 An 802.11 Wireless L A N
Notes: Figure 7.14, Page 279.
Mobile laptop computers equipped with network interface cards link to the wired LAN by communicating with the access point. The access point uses radio waves to transmit network signals from the wired network to the client adapters, which convert them to data that the mobile device can understand. The client adapter then transmits the data from the mobile device back to the access point, which forwards the data to the wired network.
This graphic illustrates an 802.11 wireless LAN operating in infrastructure mode that connects a small number of mobile devices to a larger wired LAN. Most wireless devices are client machines. The servers that the mobile client stations need to use are on the wired LAN. The access point controls the wireless stations and acts as a bridge between the main wired LAN and the wireless LAN. (A bridge connects two LANs based on different technologies like your wireless network to your BluRay player so you can download Internet movies from Netflix and watch them on your TV). The access point also controls the wireless stations.
Alt Text
Long description: An illustration explains the concept of a wireless local area network. The details of the diagram are as below:
The internet communicates to the router which in turn communicates to the wired network. The wired network includes servers, access point, and user computers.
Several laptops are shown in the wireless network of the access point.

## Slide 44: RFID and Wireless Sensor Networks (I of 3)
Radio Frequency Identification (RFID)
  Use tiny tags with microchips containing data about an item and location; tag antennas to transmit radio signals over short distances to special R F I D readers
  Common uses: Automated toll-collection; tracking goods in a supply chain
  Reduction in cost of tags making R F I D viable for many firms
Notes: This slide introduces one of two wireless technologies having a major impact on business, RFID. Ask students for examples of where RFID is used today. The text provides the example of Walmart using RFID to manage inventory and supply chains. Ask students how this works.

## Slide 45: Figure 7.15 How R F I D Works
Notes: Figure 7.15, Page 280.
RFID uses low-powered radio transmitters to read data stored in a tag at distances ranging from 1 inch to 100 feet. The reader captures the data from the tag and sends them over a network to a host computer for processing.
This graphic illustrates how RFID works. Ask students if RFID potentially poses any ethical problems. For example, if your jeans have a built in RFID chip, it’s easy to track your movements. Likewise if your student ID card has an RFID chip.
Alt Text
Long description: A sequential flow explains how RFID works. In the diagram, radio waves from a tag are shown transmitting to the RFID reader which then communicates with the host network.
The details are as below:
Tag is a microchip holds data including an identification number. The rest of the tag is an antenna that transmits data to a reader.
RFID has an antenna that constantly transmits. When it senses a tag, it wakes it up, interrogates it, and decodes the data. Then it transmits the data to a host system over wired or wireless connections.
Host computer processes the data from the tag that have been transmitted by the reader.

## Slide 46: RFID and Wireless Sensor Networks (2 of 3)
Near field communication (NFC)
  RFID-related technology that uses very short-range wireless connectivity standard
  Used by tap-and-go services such as Apple Pay, Google Pay
Notes: This slide introduces one of two wireless technologies having a major impact on business, radio frequency ID. Ask students for examples of where RFID is used today. The text provides the example of Walmart using RFID to manage inventory and supply chains. Ask students how this works.

## Slide 47: RFID and Wireless Sensor Networks (3 of 3)
Wireless Sensor Networks (WSNs)
  Networks of hundreds or thousands of interconnected wireless devices used to monitor building security, detect hazardous substances in air, monitor environmental changes, traffic, or military activity
  Devices have built-in processing, storage, and radio frequency sensors and antennas
  Require low-power, long-lasting batteries and ability to endure in the field without maintenance
  Major sources of big data and fueling Internet of Things
Notes: This slide introduces a second wireless technology having a major impact on business, wireless sensor networks. Note that the wireless sensors are linked into an interconnected network that routes the data to a computer for analysis.

## Slide 48: Figure 7.16 A Wireless Sensor Network
Notes: Figure 7.16, Page 282
The small circles represent lower-level nodes, and the larger circles represent high-end nodes. Lower-level nodes forward data to each other or to higher-level nodes, which transmit data more rapidly and speed up network performance.
This graphic illustrates the lower-level nodes and higher-level nodes at work in a wireless sensor network. Note that the server that data from the sensors is sent to acts as a gateway to a network based on Internet technology.
Alt Text
Long description: An illustration explains how a wireless sensor network works. The details are as below:
Three higher level nodes connected to each other in a triad.
Various smaller level nodes are seen forwarding the data to each other and to a higher-level node closest to the server.
The closest higher-level node is connected to the server and the server is connected to the internet.

## Slide 49: How Will M I S Help My Career?
The Company: A1 Western Car Dealers
Position Description: Automotive digital advisor
Job Requirements
Interview Questions
Author Tips
Notes: A good opportunity for a class discussion on how MIS will help students with their current or future careers. Would any in the class be interested in a job like this? What do they think are the most important skills the employer is looking for? How would they answer the interviewer questions?

## Slide 50: Copyright
This work is protected by United States copyright laws and is provided solely for the use of instructors in teaching their courses and assessing student learning. Dissemination or sale of any part of this work (including on the World Wide Web) will destroy the integrity of the work and is not permitted. The work and materials from it should never be made available to students except by instructors using the accompanying text in their classes. All recipients of this work are expected to abide by these restrictions and to honor the intended pedagogical purposes and the needs of other instructors who rely on these materials.